## Slide 1: Mathematical Methods of Uncertainty Quantification in Hydrology
Group 1: Adrien Thébault, Vincent Taneli Olander, Nafisa Raihana

## Slide 2: Presentation Overview
Parameter Optimization
Local Sensitivity Analysis
Global Sensitivity Analysis

## Slide 3: Parameter Optimization

## Slide 4: Parameter Optimization
18 parameters which are free to chose in given bounds
4 main modules in the HBV001a model
Catchment: Bavaria, short time series
Differential Evolution
Gradient Based Optimizer
Understanding the model and the optimization method
Preconsiderations

## Slide 5: Parameter Optimization
Original Code – Differential Evolution
3

## Slide 6: Parameter Optimization
Original Code – Tuning the Optimization
6

## Slide 7: Parameter Optimization
Overall Result
NSE: 0.901
Stabilizing: ~ 100 Iterations

## Slide 8: Parameter Optimization
All Parameters On
Snow initial depth: 0.000000
Snow fall/melt temperature: 0.148940
Snow melt air factor: 0.634415
Precipitation melt air factor: 0.036731
Soil initial moisture: 94.568525
Soil permanent wilting point: 432.979200
Soil field capacity: 148.866130
Soil beta: 2.659653
Storage initial upper reservoir: 1.728010
Storage initial lower reservoir: 0.739939
Upper-res. runoff split ratio: 0.748241
Percolation coefficient upper-to-lower: 0.185272
Upper-res. threshold depth: 60.579322
Upper-res. threshold coefficient: 0.143289
Upper-res. discharge to runoff coefficient: 0.000401
Upper-res. Runoff coefficient: 0.000147
Discharge rate: 0.008535
Lower-res. runoff coefficient: 0.000024

## Slide 9: Parameter Optimization
Snow Module – SNW_ATT
Convergence Plot
Scatter Plot
The Threshold Temperature turns the snow module on and off, i.e. it controls if melt occurs or not

## Slide 10: Parameter Optimization
Snow Module – SNW_AMF
Convergence Plot
Scatter Plot
The Air Temperature Melt factor (AMF) contributes to melt

## Slide 11: Parameter Optimization
Snow Module – SNW_PMF
Convergence Plot
Scatter Plot
The Precipitation Melt Air Factor (PMF) contributes to melt

## Slide 12: Parameter Optimization
Snow Module Off – Optimization Part 1
Simulated Discharge – snow modul off
Simulated Discharge – all modules on

## Slide 13: Parameter Optimization
Snow Module Off – Optimization Part 2
Schenkenau in Bavaria -> We expect melt
Less peaky as melt implies higher runoff
Interesting behavior (snow then no snow at fast melt)
High OFV
Poor convergence
Conclusion: Snow module relevant

## Slide 14: Parameter Optimization
Upper Reservoir Module – All parameters
The URR controls the fast flow only if the threshold depth is attained

## Slide 15: Parameter Optimization
Turning URR Module (fast surface flow) off
NSE = 0.8874
WSR = 0
URR_TDH​ = very large (≈1000)
TDR=0, NDR=0
ULC=1
Result:
PLN=RNF,Q_T=0,Q_N=0
URR acts as a pass-through to LRR, with no direct quickflow.

## Slide 16: Parameter Optimization
Lower Reservoir Module – LRR_DTH
Convergence Plot
Scatter Plot
The Lower Reservoir Depth gives the max. storage capacity
Internal Variables

## Slide 17: Parameter Optimization
Convergence Plot
Scatter Plot
The Lower Reservoir Discharge Efficieny factor is the fraction of water that discharges as slow baseflow
Lower Reservoir Module – LRR_DRE
Internal Variables

## Slide 18: Parameter Optimization
Lower Reservoir Module – LRR_LCT
Convergence Plot
Scatter Plot
The Lower Reservoir Cell Transfer Coef. is the fraction of water released in each step (cannot see it)
Internal Variables

## Slide 19
Turning the Lower Reservoir off
NSE: -0.1039
𝑄𝐿 = 𝐿𝑅𝑅_𝐷𝑇𝐻 × 𝐷𝑅𝐸
DRE = 0, ULC = 0, TDR = 1 (from the upper reservoir)
𝐿𝑅𝑅_𝐷𝑇𝐻 = 𝐿𝑅𝑅_𝐷𝑇𝐻 − 𝑄𝐿
𝐿𝑅𝑅_𝐷𝑇𝐻 = 𝐿𝑅𝑅_𝐷𝑇𝐻 + 𝑃𝐿𝑁
Parameter Optimization

## Slide 20: Assignment 1: Parameter Optimization
Problems which had to be overcome
  Understand exactly how Differential Evolution works to find the „optimal“ parameter
  Adapt the initial code to improve convergence
  Implement a gradient based optimizer
  Make sense of the NSE and which values do make sense and which not
  Use of log scales
  Understand the model and the given data (internal variables and geographical catchment in a lumped model)
Conclusion for the next task
  Not all parameters seem to contribute the same
  In our catchment, Lower Reservoir Module seems to play the most important role
  With our implementation, we obtain a descend NSE and simulation.
  Sensitivity Analysis useful
Conclusion and Reflexion

## Slide 21: Local Sensitivity Analysis
21

## Slide 22: Assignment 2: Local Sensitivity Analysis
Assignment 1: Found 18 optimal parameters (hopefully)
Assignment 1: URR seems less sensitive, LRR and SNOW more
First Verification of our results using local sensitivity analysis
Dimension reduction, only one parameter is varied
Expectation: Obtain parabolic OFV plot if parameter is sensitivity in the local sense
Gut feeling: Not good to vary 1 parameter in 18 dimensions
Investigating the local sensitivity of the parameters
Preconsiderations

## Slide 23: Local Sensitivity Analysis
Implementation

## Slide 24: Local Sensitivity Analysis
Result – 20% deviation

## Slide 25: Local Sensitivity Analysis
Result – whole boundaries

## Slide 26: Local Sensitivity Analysis
Snow Fall/Melt Temperature Threshold

## Slide 27: Assignment 2: Local Sensitivity Analysis
Snow Fall/Melt Temperature Threshold
Credits to Group C

## Slide 28: Local Sensitivity Analysis
Discharge Rate

## Slide 29: Assignment 2: Local Sensitivity Analysis
Discharge Rate

## Slide 30: Local Sensitivity Analysis
Precipitation Melt Factor

## Slide 31: Assignment 2 : Local Sensitivity Analysis
Precipitation Melt Factor

## Slide 32: Trying to make a sensitive parameter not sensitive
Describes the amount of snow melt induced by precipitation (if it rains, snow melts faster)
We still want to account for the effect that precipitation in form of rain increases melt
Suggestion:
  PMF does not play a role anymore
  If PPT small but SNW_DTH high => less contribution to MELT
  If PPT high(low) and SNW_DTH high(low) , i.e. the same => will be around 1, i.e. PPT does not melt whole snow instantely (PPT does not affect the melt much)
  If PPT high and SNW_DTH small => faster melt (think of muddy snow in February/March)
  If SNW_DTH = 0 no devision by zero and later on MIN(MLT,SNW_DTH) = SNW_DTH
Precipitation Melt Factor (PMF)

## Slide 33: Trying to make a sensitive parameter not sensitive
Precipitation Melt Factor (PMF) (20 % deviation)
With rewritten PMF
Without rewritten PMF
NSE: 0.8922

## Slide 34: Local Sensitivity Analysis
Soil Field Capacity

## Slide 35: Assignment 2 : Local Sensitivity Analysis
Soil Field Capacity

## Slide 36: Local Sensitivity Analysis
Soil Depth

## Slide 37: Assignment 2 :Local Sensitivity Analysis
Soil Depth

## Slide 38: Local Sensitivity Analysis
Soil Beta
Idea to make it less sensitive:
-linearization, e.g. apply natural logarithm

## Slide 39: Local Sensitivity Analysis
Percolation Coefficient Upper To Lower

## Slide 40: Local Sensitivity Analysis
Upper Reservoir Threshold Depth

## Slide 41: Assignment 2: Local Sensitivity Analysis
Problems which had to be overcome
  Understand shortcomings of local sensitivity analysis
  Understand the importance of bounds
  Beaware of the nature of the parameter (e.g. SNW_ATT)
  Try to fit the big picture
Conclusion for the next task
  Assignment 1 observations were verified
  URR not locally sensitive
  LRR parameters the most sensitive
  Soil could be rewritten, in general: It is possible to rewrite the model
  Internal variables and time series contributes a lot in the sensitivity
  Still missing the big picture: Varying all parameters to determine sensitvity (Global)
Conclusion and Reflexion

## Slide 42: Global Sensitivity Analysis
42

## Slide 43: Global Sensitivity Analysis
Assignment 1: Optimiziation to find best parameters
Assignment 2: Local sensitivity anlysis (shortcomings)
Sobol indices to get a global sensitivity
Investigating the global sensitivity of the parameters
Preconsiderations

## Slide 44: Global Sensitivity Analysis
Model setup: where is our objective function and OFV
Base: Variance based methods using Monte Carlo
Core idea: Hoeffeding decomposition:
Here:
Apply this to the our OFV
First-order (main effect):
Total-effect (main + all interactions):
Paper Satelli et al. – theoretical background
„Expected reduction in variance that would be obtained if could be fixed“
„Expected variance that would be left if all factors but could be fixed“

## Slide 45: Global Sensitivity Analysis
Setup Code

## Slide 46: Global Sensitivity Analysis
Sobol Sampling

## Slide 47: Global Sensitivity Analysis

## Slide 48: Global Sensitivity Analysis
Sobol Sampling

## Slide 49: Global Sensitivity Analysis

## Slide 50: Global Sensitivity Analysis
Sobol Sampling

## Slide 51: Global Sensitivity Analysis
Sobol Sampling – Full Range
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE
snw_dth | 0.0108 | 0.0 | 0.0075 | 0.0
snw_att | 0.0113 | 0.002 | 0.4568 | 0.4642
snw_pmf | 0.0108 | 0.0 | 0.0076 | 0.0
snw_amf | 0.0106 | 0.0006 | 0.0078 | 0.0006
sl0_dth | 0.011 | 0.0004 | 0.0286 | 0.0275
sl0_pwp | 0.0108 | 0.0 | 0.0076 | 0.0002
sl0_fcy | 0.0141 | 0.0042 | 0.0925 | 0.1345
sl0_bt0 | 0.0112 | 0.001 | 0.141 | 0.1865
urr_dth | 0.0408 | 0.026 | 0.0075 | 0.0
lrr_dth | 0.3807 | 0.5895 | 0.0075 | 0.0
urr_wsr | 0.0108 | 0.0 | 0.0083 | 0.001
urr_ulc | 0.0107 | 0.0042 | 0.0144 | 0.0286
urr_tdh | 0.0104 | 0.0006 | 0.0076 | 0.0
urr_tdr | 0.011 | 0.0003 | 0.0076 | 0.0
urr_ndr | 0.0163 | 0.0103 | 0.0259 | 0.0379
urr_uct | 0.0108 | 0.0001 | 0.0162 | 0.039
lrr_dre | 0.3697 | 0.587 | 0.0401 | 0.1082
lrr_lct | 0.0114 | 0.0018 | 0.0778 | 0.1424
SUM | 0,9632 | 1,2280 | 0,9623 | 1,1706

## Slide 52: Global Sensitivity Analysis
Sobol Sampling – Narrow Range
Parameter | S1_Narrow_NSE | ST_Narrow_NSE | S1_Narrow_LnNSE | ST_Narrow_LnNSE
snw_dth | 0.0 | 0.0 | 0.0006 | 0.0
snw_att | 0.0 | 0.0 | 0.0006 | 0.0
snw_pmf | 0.0964 | 0.1563 | 0.0006 | 0.0005
snw_amf | 0.0027 | 0.0508 | 0.0028 | 0.0028
sl0_dth | 0.0263 | 0.2996 | 0.0022 | 0.0209
sl0_pwp | 0.0 | 0.0003 | 0.0006 | 0.0
sl0_fcy | 0.1948 | 0.5856 | 0.0147 | 0.0344
sl0_bt0 | 0.0025 | 0.0139 | 0.0005 | 0.0043
urr_dth | 0.0003 | 0.0003 | 0.0012 | 0.0007
lrr_dth | 0.0001 | 0.0 | 0.0008 | 0.0001
urr_wsr | 0.0001 | 0.0003 | 0.0006 | 0.0
urr_ulc | -0.0011 | 0.0122 | 0.0009 | 0.0003
urr_tdh | 0.0 | 0.0 | 0.0006 | 0.0
urr_tdr | 0.0 | 0.0 | 0.0006 | 0.0
urr_ndr | 0.0 | 0.0 | 0.0006 | 0.0
urr_uct | -0.0 | 0.0 | 0.0006 | 0.0
lrr_dre | 0.1825 | 0.3823 | 0.9566 | 0.9585
lrr_lct | 0.0 | 0.0 | 0.0007 | 0.0
SUM | 0,5046 | 1,5016 | 0,9858 | 1,0225

## Slide 53: Global Sensitivity Analysis
NSE versus LN-NSE
Nash Sutcliffe Efficiency
Log Nash Sutcliffe Efficiency
Small simulated discharges are enhanced in log
Large flows take less influence
If observation and simulation differs a lot, log amplifies

## Slide 54: Global Sensitivity Analysis
Comparing the Effect of Objective Function

## Slide 55: Global Sensitivity Analysis
Comparing Effect of Parameter Range

## Slide 56: Global Sensitivity Analysis
  Problems which had to be overcome
  Understand the difference between first- and total-order-indices
  Understand the importance of bounds
  Beaware of the nature of the parameter (e.g. SNW_ATT)
  Try to fit the big picture
  Runtime
Conclusion and Reflexion

## Slide 57: Big Picture: Combining All 3 Assignments
42

## Slide 58: Big Picture: Combining All 3 Assignments
Discharge Rate
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE
lrr_dre | 0.3697 | 0.587 | 0.0401 | 0.1082

## Slide 59: Big Picture: Combining All 3 Assignments
Upper Reservoir Threshold Depth
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE
urr_tdh | 0.0104 | 0.0006 | 0.0076 | 0.0

## Slide 60: Big Picture: Combining All 3 Assignments
Soil field capacity
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE
sl0_fcy | 0.0141 | 0.0042 | 0.0925 | 0.1345

## Slide 61: Big Picture: Combining All 3 Assignments
Soil depth
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE
snw_dth | 0.0108 | 0.0 | 0.0075 | 0.0

## Slide 62: Big Picture: Combining All 3 Assignments
Snow Melt Temperature Threshold
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE
snw_att | 0.0113 | 0.002 | 0.4568 | 0.4642

## Slide 63: Big Picture: Combining All 3 Assignments
Precipitation Melt Factor
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE
snw_pmf | 0.0108 | 0.0 | 0.0076 | 0.0

## Slide 64: Big Picture: Combining All 3 Assignments
Lower and Upper reservoir parameters:
lrr_dre: HIGH in both NSE (blue ~0.6) and LnNSE (green ~0.5)
urr_tdh: same for both metrics. This parameter is neligible.
Snow parameters:
snw_att: MUCH higher with LnNSE (green ~0.5) than NSE (blue ~0.0)
Snw_pmf: this parameter becomes moderately important for peak matching (NSE) but remains unimportant for baseflow/low flows (LnNSE).
Soil parameters:
Soil_fcy: Similar in both (green ~0.15, blue small)
Soil_dth: soil depth becomes critical for matching peaks with NSE but remains unimportant for matching low flows with LnNSE.

## Slide 65: Big Picture: Combining All 3 Assignments
Parameters Important for both NSE and LnNSE (Globally Important):
lrr_dre (baseflow discharge) - controls both peaks and recessions
Parameters Important only for NSE (Peak-Specific):
sl0_dth (soil depth) - affects peak storage/generation
snw_pmf (precip melt factor) - affects snowmelt peak amplification
sl0_fcy (soil field capacity) - affects infiltration during events
Parameters Important only for LnNSE (Baseflow-Specific):
snw_att (snow temp threshold) - affects when baseflow season starts
Parameters Important for neither (Negligible):
urr_tdh and other URR parameters

## Slide 66: Key Findings & Conclusions
✓ Successful calibration (NSE = 0.901) using Differential Evolution
✓ Snow and lower reservoir modules are critical for model performance
✓ Soil field capacity and discharge rate show highest local sensitivity
✓ Global sensitivity analysis reveals important parameter interactions

## Slide 67
Thank You!