## Slide 1: Mathematical Methods of Uncertainty Quantification in Hydrology
Assignment 1,2 & 3: Parameter Optimization, Local Sensitivity Analysis & Global Sensitivity Analysis
Group 1: Adrien Thébault, Vincent Taneli Olander, Nafisa Raihana

## Slide 2: Parameter Optimization

## Slide 3: Parameter Optimization
Original Code

## Slide 4: Parameter Optimization
NSE: 0.901
Stabilizing: ~ 100 Iterations
All Parameters On

## Slide 5: Parameter Optimization
Snow initial depth: 0.000000
Snow fall/melt temperature: 0.148940
Snow melt air factor: 0.634415
Precipitation melt air factor: 0.036731
Soil initial moisture: 94.568525
Soil permanent wilting point: 432.979200
Soil field capacity: 148.866130
Soil beta: 2.659653
Storage initial upper reservoir: 1.728010
Storage initial lower reservoir: 0.739939
Upper-res. runoff split ratio: 0.748241
Percolation coefficient upper-to-lower: 0.185272
Upper-res. threshold depth: 60.579322
Upper-res. threshold coefficient: 0.143289
Upper-res. discharge to runoff coefficient: 0.000401
Upper-res. Runoff coefficient: 0.000147
Discharge rate: 0.008535
Lower-res. runoff coefficient: 0.000024
All Parameters On

## Slide 6: Parameter Optimization
Snow Module
Snow initial depth
Snow fall/melt temperature threshold

## Slide 7: Parameter Optimization
Snow Module
Snow melt air factor
Precipitation melt air factor

## Slide 8: Parameter Optimization
Snow Module Off – Optimization Part 1
Simulated Discharge – snow modul off
Simulated Discharge – all modules on
We set TT = -100°C
We set AMF = PMF = 0
Adapt bounds and run optimization

## Slide 9: Parameter Optimization
Snow Module Off – Optimization Part 2
Schenkenau in Bavaria -> We expect melt
Less peaky as melt implies higher runoff
Interesting behavior (snow then no snow at fast melt)
High OFV
Poor convergence
Conclusion: Snow module relevant

## Slide 10: Parameter Optimization
Lower Reservoir Off
Storage initial lower reservoir
Discharge rate

## Slide 11: Parameter Optimization
Lower reservoir off
NSE: -0.1039
𝑄𝐿 = 𝐿𝑅𝑅_𝐷𝑇𝐻 × 𝐷𝑅𝐸 DRE = 0, ULC = 0, TDR = 1 (from the upper reservoir)
𝐿𝑅𝑅_𝐷𝑇𝐻 = 𝐿𝑅𝑅_𝐷𝑇𝐻 − 𝑄𝐿
𝐿𝑅𝑅_𝐷𝑇𝐻 = 𝐿𝑅𝑅_𝐷𝑇𝐻 + 𝑃𝐿𝑁

## Slide 12: Parameter Optimization
Lower Reservoir Off
Lower-res. runoff coefficient

## Slide 13: Local Sensitivity Analysis

## Slide 14: Preconsiderations
Logarithmic and clipped y-axis
Maximal evaluations up to 60 000
Adjusted tolerances
More exploration (mutation & recombination)
Initial parameter adapted
Minimization method
Adaption of previous errors to allow for better local sensitivity analysis
Updated First Assignment

## Slide 15: Local Sensitivity Analysis
Implementation

## Slide 16: Local Sensitivity Analysis
Result – 20% deviation

## Slide 17: Local Sensitivity Analysis
Result – whole boundaries

## Slide 18: Local Sensitivity Analysis
Snow Fall/Melt Temperature Threshold

## Slide 19: Local Sensitivity Analysis
Soil Field Capacity

## Slide 20: Local Sensitivity Analysis
Discharge Rate

## Slide 21: Local Sensitivity Analysis
Precipitation Melt Factor

## Slide 22: Trying to make a sensitive parameter not sensitive
Describes the amount of snow melt induced by precipitation (if it rains, snow melts faster)
We still want to account for the effect that precipitation in form of rain increases melt
Suggestion:
  PMF does not play a role anymore
  If PPT small but SNW_DTH high => less contribution to MELT
  If PPT high(low) and SNW_DTH high(low) , i.e. the same => will be around 1, i.e. PPT does not melt whole snow instantely (PPT does not affect the melt much)
  If PPT high and SNW_DTH small => faster melt (think of muddy snow in February/March)
  If SNW_DTH = 0 no devision by zero and later on MIN(MLT,SNW_DTH) = SNW_DTH
Precipitation Melt Factor (PMF)

## Slide 23: Local Sensitivity Analysis
Soil Depth

## Slide 24: Local Sensitivity Analysis
Soil Beta
Idea to make it less sensitive:
-linearization, e.g. apply natural logarithm

## Slide 25: Recall Assignment 1
Turning URR Module (fast surface flow) off had the least impact
NSE = 0.8874
WSR = 0
URR_TDH​ = very large (≈1000)
TDR=0, NDR=0
ULC=1
Result:
PLN=RNF,Q_T=0,Q_N=0
URR acts as a pass-through to LRR, with no direct quickflow.

## Slide 26: Local Sensitivity Analysis
Percolation Coefficient Upper To Lower

## Slide 27: Local Sensitivity Analysis
Upper Reservoir Threshold Depth

## Slide 28: Global Sensitivity Analysis

## Slide 29: Global Sensitivity Analysis
Setup Code

## Slide 30: Global Sensitivity Analysis
Sobol Sampling

## Slide 31: Global Sensitivity Analysis
Sobol Sampling

## Slide 32: Global Sensitivity Analysis
Sobol Sampling

## Slide 33: Global Sensitivity Analysis
Sobol Sampling

## Slide 34: Global Sensitivity Analysis
Sobol Sampling

## Slide 35: Global Sensitivity Analysis
Sobol Sampling

## Slide 36: Global Sensitivity Analysis
Sobol Sampling