## Slide 1: Mathematical Methods of Uncertainty Quantification in Hydrology
Assignment 1,2 & 3: Parameter Optimization, Local Sensitivity Analysis & Global Sensitivity Analysis
Group 1: Adrien Thébault, Vincent Taneli Olander, Nafisa Raihana

## Slide 2: Assignment 1: Parameter Optimization

## Slide 3: Assignment 1: Parameter Optimization
18 parameters which are free to chose in given bounds
4 main modules in the HBV001a model
Catchment: Bavaria, short time series
Differential Evolution
Gradient Based Optimizer
Understanding the model and the optimization method
Preconsiderations

## Slide 4: Assignment 1: Parameter Optimization
Original Code – The Differential Evolution

## Slide 5: Assignment 1: Parameter Optimization
Original Code – Tuning The Optimization

## Slide 6: Assignment 1: Parameter Optimization
NSE: 0.901
Stabilizing: ~ 100 Iterations
Overall Result

## Slide 7: Assignment 1: Parameter Optimization
Snow initial depth: 0.000000
Snow fall/melt temperature: 0.148940
Snow melt air factor: 0.634415
Precipitation melt air factor: 0.036731
Soil initial moisture: 94.568525
Soil permanent wilting point: 432.979200
Soil field capacity: 148.866130
Soil beta: 2.659653
Storage initial upper reservoir: 1.728010
Storage initial lower reservoir: 0.739939
Upper-res. runoff split ratio: 0.748241
Percolation coefficient upper-to-lower: 0.185272
Upper-res. threshold depth: 60.579322
Upper-res. threshold coefficient: 0.143289
Upper-res. discharge to runoff coefficient: 0.000401
Upper-res. Runoff coefficient: 0.000147
Discharge rate: 0.008535
Lower-res. runoff coefficient: 0.000024
Detailed Parameters and internal variables

## Slide 8: Assignment 1: Parameter Optimization
Snow Module – SNW_ATT
Convergence Plot
Scatter Plot
The Threshold Temperature turns the snow module on and off, i.e. it controls if melt occurs or not

## Slide 9: Assignment 1: Parameter Optimization
Snow Module – SNW_AMF
Convergence Plot
Scatter Plot
The Air Temperature Melt factor (AMF) contributes to melt

## Slide 10: Assignment 1: Parameter Optimization
Snow Module – SNW_PMF
Convergence Plot
Scatter Plot
The Precipitation Melt Air Factor (PMF) contributes to melt

## Slide 11: Assignment 1: Parameter Optimization
Snow Module Off – Optimization Part 1
Simulated Discharge – snow modul off
Simulated Discharge – all modules on
We set TT = -100°C
We set AMF = PMF = 0
Adapt bounds and run optimization

## Slide 12: Assignment 1: Parameter Optimization
Snow Module Off – Optimization Part 2
Schenkenau in Bavaria -> We expect melt
Less peaky as melt implies higher runoff
Interesting behavior (snow then no snow at fast melt)
High OFV
Poor convergence
Conclusion: Snow module relevant

## Slide 13: Assignment 1: Parameter Optimization
Upper Reservoir Module – All parameters
The URR controls the fast flow only if the threshold depth is attained

## Slide 14: Assignment 1: Parameter Optimization
Turning URR Module (fast surface flow) off
NSE = 0.8874
WSR = 0
URR_TDH​ = very large (≈1000)
TDR=0, NDR=0
ULC=1
Result:
PLN=RNF,Q_T=0,Q_N=0
URR acts as a pass-through to LRR, with no direct quickflow.

## Slide 15: Assignment 1: Parameter Optimization
Lower Reservoir Module – LRR_DTH
Convergence Plot
Scatter Plot
The Lower Reservoir Depth gives the max. storage capacity
Internal Variables

## Slide 16: Assignment 1: Parameter Optimization
Lower Reservoir Module – LRR_DRE
Convergence Plot
Scatter Plot
The Lower Reservoir Discharge Efficieny factor is the fraction of water that discharges as slow baseflow
Internal Variables

## Slide 17: Assignment 1: Parameter Optimization
Lower Reservoir Module – LRR_LCT
Convergence Plot
Scatter Plot
The Lower Reservoir Cell Transfer Coef. is the fraction of water released in each step (cannot see it)
Internal Variables

## Slide 18: Assignment 1: Parameter Optimization
Turning the Lower Reservoir off
NSE: -0.1039
𝑄𝐿 = 𝐿𝑅𝑅_𝐷𝑇𝐻 × 𝐷𝑅𝐸 DRE = 0, ULC = 0, TDR = 1 (from the upper reservoir)
𝐿𝑅𝑅_𝐷𝑇𝐻 = 𝐿𝑅𝑅_𝐷𝑇𝐻 − 𝑄𝐿
𝐿𝑅𝑅_𝐷𝑇𝐻 = 𝐿𝑅𝑅_𝐷𝑇𝐻 + 𝑃𝐿𝑁

## Slide 19: Assignment 1: Parameter Optimization
Problems which had to be overcome
  Understand exactly how Differential Evolution works to find the „optimal“ parameter
  Adapt the initial code to improve convergence
  Implement a gradient based optimizer
  Make sense of the NSE and which values do make sense and which not
  Use of log scales
  Understand the model and the given data (internal variables and geographical catchment in a lumped model)
Conclusion for the next task
  Not all parameters seem to contribute the same
  In our catchment, Lower Reservoir Module seems to play the most important role
  With our implementation, we obtain a descend NSE and simulation.
  Sensitivity Analysis useful
Conclusion and Reflexion

## Slide 20: Assignment 2: Local Sensitivity Analysis

## Slide 21: Assignment 2: Local Sensitivity Analysis
Assignment 1: Found 18 optimal parameters (hopefully)
Assignment 1: URR seems less sensitive, LRR and SNOW more
First Verification of our results using local sensitivity analysis
Dimension reduction, only one parameter is varied
Expectation: Obtain parabolic OFV plot if parameter is sensitivity in the local sense
Gut feeling: Not good to vary 1 parameter in 18 dimensions
Investigating the local sensitivity of the parameters
Preconsiderations

## Slide 22: Assignment 2: Local Sensitivity Analysis
Implementation

## Slide 23: Assignemnt 2: Local Sensitivity Analysis
Result – 20% deviation

## Slide 24: Assignement 2: Local Sensitivity Analysis
Result – whole boundaries

## Slide 25: Assignment 2: Local Sensitivity Analysis
Snow Fall/Melt Temperature Threshold

## Slide 26: Assignment 2: Local Sensitivity Analysis
Snow Fall/Melt Temperature Threshold
Credits to Group C

## Slide 27: Assignment 2: Local Sensitivity Analysis
Discharge Rate

## Slide 28: Assignment 2: Local Sensitivity Analysis
Discharge Rate

## Slide 29: Assignment 2 : Local Sensitivity Analysis
Precipitation Melt Factor

## Slide 30: Assignment 2 : Local Sensitivity Analysis
Precipitation Melt Factor

## Slide 31: Trying to make a sensitive parameter not sensitive
Describes the amount of snow melt induced by precipitation (if it rains, snow melts faster)
We still want to account for the effect that precipitation in form of rain increases melt
Suggestion:
  PMF does not play a role anymore
  If PPT small but SNW_DTH high => less contribution to MELT
  If PPT high(low) and SNW_DTH high(low) , i.e. the same => will be around 1, i.e. PPT does not melt whole snow instantely (PPT does not affect the melt much)
  If PPT high and SNW_DTH small => faster melt (think of muddy snow in February/March)
  If SNW_DTH = 0 no devision by zero and later on MIN(MLT,SNW_DTH) = SNW_DTH
Precipitation Melt Factor (PMF)

## Slide 32: Trying to make a sensitive parameter not sensitive
Precipitation Melt Factor (PMF) (20 % deviation)
With rewritten PMF
Without rewritten PMF

## Slide 33: Assignment 2 : Local Sensitivity Analysis
Soil Field Capacity

## Slide 34: Assignment 2 : Local Sensitivity Analysis
Soil Field Capacity

## Slide 35: Assignment 2 :Local Sensitivity Analysis
Soil Depth

## Slide 36: Assignment 2 :Local Sensitivity Analysis
Soil Depth

## Slide 37: Assignment 2 : Local Sensitivity Analysis
Soil Beta
Idea to make it less sensitive:
-linearization, e.g. apply natural logarithm

## Slide 38: Assignement 2: Local Sensitivity Analysis
Percolation Coefficient Upper To Lower

## Slide 39: Assignemnt 2: Local Sensitivity Analysis
Upper Reservoir Threshold Depth

## Slide 40: Assignment 2: Local Sensitivity Analysis
Problems which had to be overcome
  Understand shortcomings of local sensitivity analysis
  Understand the importance of bounds
  Beaware of the nature of the parameter (e.g. SNW_ATT)
  Try to fit the big picture
Conclusion for the next task
  Assignment 1 observations were verified
  URR not locally sensitive
  LRR parameters the most sensitive
  Soil could be rewritten, in general: It is possible to rewrite the model
  Internal variables and time series contributes a lot in the sensitivity
  Still missing the big picture: Varying all parameters to determine sensitvity (Global)
Conclusion and Reflexion

## Slide 41: Assignment 3: Global Sensitivity Analysis

## Slide 42: Assignment 3: Global Sensitivity Analysis
Assignment 1: Optimiziation to find best parameters
Assignment 2: Local sensitivity anlysis (shortcomings)
Goal: Determining global sensitivity, i.e. how much variation in all input parameters affect the variability of the model output
Sobol indices
Investigating the global sensitivity of the parameters
Preconsiderations

## Slide 43: Assignment 3: Global Sensitivity Analysis
Model setup: where is our objective function and OFV
Base: Variance based methods using MC
Core idea: Hoeffeding decomposition:
Here:
Radial sampling:
Two approximation (Jansen)
Paper Satelli et al. – theoretical background

## Slide 44: Assignment 3: Global Sensitivity Analysis
Setup Code

## Slide 45: Assignemnt 3: Global Sensitivity Analysis
Sobol Sampling

## Slide 46: Assignment 3: Global Sensitivity Analysis
Sobol Sampling

## Slide 47: Global Sensitivity Analysis
Sobol Sampling
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE | S1_Narrow_NSE | ST_Narrow_NSE | S1_Narrow_LnNSE | ST_Narrow_LnNSE
snw_dth | 0.0108 | 0.0 | 0.0075 | 0.0 | 0.0 | 0.0 | 0.0006 | 0.0
snw_att | 0.0113 | 0.002 | 0.4568 | 0.4642 | 0.0 | 0.0 | 0.0006 | 0.0
snw_pmf | 0.0108 | 0.0 | 0.0076 | 0.0 | 0.0964 | 0.1563 | 0.0006 | 0.0005
snw_amf | 0.0106 | 0.0006 | 0.0078 | 0.0006 | 0.0027 | 0.0508 | 0.0028 | 0.0028
sl0_dth | 0.011 | 0.0004 | 0.0286 | 0.0275 | 0.0263 | 0.2996 | 0.0022 | 0.0209
sl0_pwp | 0.0108 | 0.0 | 0.0076 | 0.0002 | 0.0 | 0.0003 | 0.0006 | 0.0
sl0_fcy | 0.0141 | 0.0042 | 0.0925 | 0.1345 | 0.1948 | 0.5856 | 0.0147 | 0.0344
sl0_bt0 | 0.0112 | 0.001 | 0.141 | 0.1865 | 0.0025 | 0.0139 | 0.0005 | 0.0043
urr_dth | 0.0408 | 0.026 | 0.0075 | 0.0 | 0.0003 | 0.0003 | 0.0012 | 0.0007
lrr_dth | 0.3807 | 0.5895 | 0.0075 | 0.0 | 0.0001 | 0.0 | 0.0008 | 0.0001
urr_wsr | 0.0108 | 0.0 | 0.0083 | 0.001 | 0.0001 | 0.0003 | 0.0006 | 0.0
urr_ulc | 0.0107 | 0.0042 | 0.0144 | 0.0286 | -0.0011 | 0.0122 | 0.0009 | 0.0003
urr_tdh | 0.0104 | 0.0006 | 0.0076 | 0.0 | 0.0 | 0.0 | 0.0006 | 0.0
urr_tdr | 0.011 | 0.0003 | 0.0076 | 0.0 | 0.0 | 0.0 | 0.0006 | 0.0
urr_ndr | 0.0163 | 0.0103 | 0.0259 | 0.0379 | 0.0 | 0.0 | 0.0006 | 0.0
urr_uct | 0.0108 | 0.0001 | 0.0162 | 0.039 | -0.0 | 0.0 | 0.0006 | 0.0
lrr_dre | 0.3697 | 0.587 | 0.0401 | 0.1082 | 0.1825 | 0.3823 | 0.9566 | 0.9585
lrr_lct | 0.0114 | 0.0018 | 0.0778 | 0.1424 | 0.0 | 0.0 | 0.0007 | 0.0
Just the draft

## Slide 48: Assignment 3: Global Sensitivity Analysis
Sobol Sampling
Parameter | S1_Full_NSE | ST_Full_NSE | S1_Full_LnNSE | ST_Full_LnNSE
snw_dth | 0.0108 | 0.0 | 0.0075 | 0.0
snw_att | 0.0113 | 0.002 | 0.4568 | 0.4642
snw_pmf | 0.0108 | 0.0 | 0.0076 | 0.0
snw_amf | 0.0106 | 0.0006 | 0.0078 | 0.0006
sl0_dth | 0.011 | 0.0004 | 0.0286 | 0.0275
sl0_pwp | 0.0108 | 0.0 | 0.0076 | 0.0002
sl0_fcy | 0.0141 | 0.0042 | 0.0925 | 0.1345
sl0_bt0 | 0.0112 | 0.001 | 0.141 | 0.1865
urr_dth | 0.0408 | 0.026 | 0.0075 | 0.0
lrr_dth | 0.3807 | 0.5895 | 0.0075 | 0.0
urr_wsr | 0.0108 | 0.0 | 0.0083 | 0.001
urr_ulc | 0.0107 | 0.0042 | 0.0144 | 0.0286
urr_tdh | 0.0104 | 0.0006 | 0.0076 | 0.0
urr_tdr | 0.011 | 0.0003 | 0.0076 | 0.0
urr_ndr | 0.0163 | 0.0103 | 0.0259 | 0.0379
urr_uct | 0.0108 | 0.0001 | 0.0162 | 0.039
lrr_dre | 0.3697 | 0.587 | 0.0401 | 0.1082
lrr_lct | 0.0114 | 0.0018 | 0.0778 | 0.1424
SUM | 0,9632 | 1,2280 | 0,9623 | 1,1706

## Slide 49: Assignment 3: Global Sensitivity Analysis
NSE versus LN-NSE
Nash Sutcliffe Efficiency
Log Nash Sutcliffe Efficiency
Small simulated discharges are enhanced in log
Large flows take less influence
If observation and simulation differs a lot, log amplifies

## Slide 50: Global Sensitivity Analysis
Sobol Sampling
Parameter | S1_Narrow_NSE | ST_Narrow_NSE | S1_Narrow_LnNSE | ST_Narrow_LnNSE
snw_dth | 0.0 | 0.0 | 0.0006 | 0.0
snw_att | 0.0 | 0.0 | 0.0006 | 0.0
snw_pmf | 0.0964 | 0.1563 | 0.0006 | 0.0005
snw_amf | 0.0027 | 0.0508 | 0.0028 | 0.0028
sl0_dth | 0.0263 | 0.2996 | 0.0022 | 0.0209
sl0_pwp | 0.0 | 0.0003 | 0.0006 | 0.0
sl0_fcy | 0.1948 | 0.5856 | 0.0147 | 0.0344
sl0_bt0 | 0.0025 | 0.0139 | 0.0005 | 0.0043
urr_dth | 0.0003 | 0.0003 | 0.0012 | 0.0007
lrr_dth | 0.0001 | 0.0 | 0.0008 | 0.0001
urr_wsr | 0.0001 | 0.0003 | 0.0006 | 0.0
urr_ulc | -0.0011 | 0.0122 | 0.0009 | 0.0003
urr_tdh | 0.0 | 0.0 | 0.0006 | 0.0
urr_tdr | 0.0 | 0.0 | 0.0006 | 0.0
urr_ndr | 0.0 | 0.0 | 0.0006 | 0.0
urr_uct | -0.0 | 0.0 | 0.0006 | 0.0
lrr_dre | 0.1825 | 0.3823 | 0.9566 | 0.9585
lrr_lct | 0.0 | 0.0 | 0.0007 | 0.0
SUM | 0,5046 | 1,5016 | 0,9858 | 1,0225

## Slide 51: Global Sensitivity Analysis
Sobol Sampling

## Slide 52: Global Sensitivity Analysis
Sobol Sampling

## Slide 53: Global Sensitivity Analysis
Sobol Sampling

## Slide 54: Assignment 3: Gloabl Sensitivity Analysis
Problems which had to be overcome
  Understand shortcomings of local sensitivity analysis
  Understand the importance of bounds
  Beaware of the nature of the parameter (e.g. SNW_ATT)
  Try to fit the big picture
Conclusion for the next task
  Assignment 1 observations were verified
  URR not locally sensitive
  LRR parameters the most sensitive
  Soil could be rewritten, in general: It is possible to rewrite the model
  Internal variables and time series contributes a lot in the sensitivity
  Still missing the big picture: Varying all parameters to determine sensitvity (Global)
Conclusion and Reflexion

## Slide 55: Big picture: Combining the 3 assignments

## Slide 56
COMPARING the result of local and global sensitivity

## Slide 57
Interpret everything, take e.g. 6 parameter and put everything together
Explain the differences in ln NSE and NSE